## 4.3 Winter Pilot Study 2005

### Overview

The purpose of this pilot study is to comply with an NPDES permit provision for ambient water monitoring for dischargers in the San Francisco Bay area.  Estuarine water will be sampled at three historical RMP stations (i.e., Sacramento River (BG20), Yerba Buena Island (BC10), and Dumbarton Bridge (BA30)) during the 2005 winter season (February 2005).   These water samples will be analyzed for contaminants on the California Toxics Rule priority pollutant list (see Table 1 for a complete list).

Wet weather Status & Trends contaminant monitoring is an important element of the RMP.  At the present time, the S&T program, occurs during the dry season; inter-annual variation is not captured by this sampling plan.  The results from this pilot study will provide the Water Board with important wet weather contaminant information from the three RMP sampling locations used in the NPDES permitting process that have not been monitored since 2001.

Seasonal contaminant monitoring results from the RMP have been an important resource provided to environmental managers of Region 2 for use in NPDES permitting and the 303(d) listing processes.  This Pilot Study is in interim monitoring effort put in place until the TRC and a specialized work group can convene to evaluate the S&T Program design in light of several pending monitoring issues including addressing the new RMP Management Questions.

The TRC and a new RMP S&T work-group (or a similar group) should convene late in 2005 to begin discussions on how the RMP should address long-term contaminant monitoring of the Estuary including the need for a seasonal monitoring component.  Additional tasks pending for the work-group to address are:  the frequency and best time and locations for monitoring aquatic toxicity (seeing as the RMP has seen very little aquatic toxicity in the Estuary al large in recent years and decreasing incidences of aquatic toxicity in the tributaries on an episodic storm-event based sampling design), how to get a better handle on the persistent sediment toxicity observed in the Estuary (Pulse-2004 reported an average of 60% of the samples were toxic to at least one test species), and a review the current sampling design (i.e. the number of samples allocated per Estuary region for water and sediment monitoring,  frequency for monitoring legacy and new and emerging contaminants of concern (currently the South Bay and Lower South Bay have a lot more water samples allocated to them), and review of the current parameter list (do all parameters need to measured each cruise as some parameters show little trend over time).

### Approach

SFEI will serve as a coordinator for executing this work plan.  Current RMP S&T sub-contractors will provide services for this study to ensure consistency in sampling and analytical methods with the RMP S&T Monitoring Program.

This project will require execution of the following tasks.

- Project Management and Coordination.  SFEI will develop subcontracts, coordinate, track deliverables, and develop specify appropriate data reporting and quality assurance procedures.

- Sample Collection.  This task will be conducted by SFEI and/or subcontractors.

- Sample Extraction, Quantification, and Data reporting.  After receipt of samples, the analytical laboratory will analyze samples in accord with conditions agreed to in the contract, including data quality objectives, turnaround time, reporting formats, and specific quality assurance samples and procedures.

- Reporting.  The data from this study will be made available as part of the RMP S&T program.  The results will be reported in the Water Monitoring chapter of the 2005 RMP Annual Monitoring Results.

Water will be collected at three historical RMP stations and analyzed for trace elements and trace organics samples.  A CTD profile is made at each water station according to the RMP QAPP.

Applied Marine Sciences will provide logistical and sampling support for the Wet Season Pilot Study sampling cruise. The University of California at Santa Cruz Environmental Toxicology Laboratory will sample and analyze for trace elements and ancillary parameters.  AXYS Analytical will analyze for trace organics. SFEI will collect water samplers using an XAD sampler.  Water hardness will be analyzed by BACWA laboratories.

### Staff Involved

SFEI staff involved with this task include:  Sarah Lowe, Don Yee, Meg Sedlak, and Jen Hunt.  Oversight will be conducted by the RMP Redesign Workgroup and Regional Board staff (e.g. Karen Taberski, Lila Tang).

### Schedule and Deliverables

| Deliverable | Target Date |
| --- | --- |
| Data made available on the RMP Data Access Website | Fall 2005 |
| Convene the Re-design workgroup to discuss long-term monitoring considerations with in the S&T program | Winter 2005 |
| Reporting as part of the 2005 RMP Annual Monitoring Results | April 2006 |

### Budget

SFEI labor cost to conduct this task is approximately $18,000.  Current Subcontract cost estimate is approximately $55,000.  The total budget approved for this task is $100,000.

## Table 1.  Parameter List, Contracting Laboratories, and Target Method Detection Limits (MDLs) for the 2005 RMP Winter Pilot Study.

| Conventional Water Quality Parameters | Lab(s) | Reporting Units |
| --- | --- | --- |
|  | Conductivity | AMS/UCSCDET | µmho |
|  | Dissolved Ammonia | UCSCDET | mg/L (N) |
|  | Dissolved Nitrate | UCSCDET | mg/L (N) |
|  | Dissolved Nitrite | UCSCDET | mg/L (N) |
|  | Dissolved Organic Carbon | UCSCDET | µg/L |
|  | Particulate Organic Carbon (new in 2004) | UCSCDET? | mg/Kg |
|  | Dissolved Oxygen | UCSCDET | mg/L |
|  | Dissolved Phosphates | UCSCDET | mg/L |
|  | Dissolved Silicates | UCSCDET | mg/L |
|  | Hardness (when salinity is < 5 o/oo) | USD | mg/L (CaCO3) |
|  | PH | AMS/UCSCDET | pH |
|  | Phaeophytin | UCSCDET | mg/m3 |
|  | Salinity (by salinometer) | UCSCDET | psu |
|  | Salinity (by SCT) | AMS/UCSCDET | ‰ |
|  | Temperature | AMS/UCSCDET | °C |
|  | Total Chlorophyll-a | UCSCDET | mg/m3 |
|  | Total Suspended Solids | UCSCDET | mg/L |

| Trace elements analyzed in water: Target Method Detection Limits (MDLs) are in parentheses following the reporting units. |
| --- |
|  | Water (Dissolved and Total) |  |  |  |
| Lab(s) | BRL/UCSCDET |  |  |  |
| Arsenic (As) | µg/L (0.1) |  |  |  |
| Cadmium (Cd)* | µg/L(0.001) |  |  |  |
| Cobalt (Co)* | µg/L(0.001) |  |  |  |
| Copper (Cu)* | µg/L (0.01) |  |  |  |
| Iron (Fe)* | µg/L(10) |  |  |  |
| Lead (Pb)* | µg/L (0.001) |  |  |  |
| Manganese (Mn)* | µg/L (0.01) |  |  |  |
| Mercury (Hg) | µg/L (.0001) |  |  |  |
| Methylmercury (MeHg) | ng/L (0.005) |  |  |  |
| Nickel (Ni)* | µg/L (0.01) |  |  |  |
| Selenium (Se) | µg/L (0.02) |  |  |  |
| Silver (Ag)* | µg/L (0.0001) |  |  |  |
| Zinc (Zn)* | µg/L (0.005) |  |  |  |

* Near-total instead of total concentrations are reported for water.  Near-total metals are extracted with a weak acid (pH < 2) for a minimum of one month, resulting in measurements that approximate bioavailability of these metals to Estuary organisms.

## Table 1 (continued). Parameter List, Contracting Laboratories, and Target MDLs

| Trace organic parameters (lab; reporting units) – in water (AXYS & CDFG; pg/L) samples: Organochlorines analyzed by GC-ECD will be determined using two columns of differing polarity. |
| --- |
| PAHS (Target MDLs: water – 200 pg/L, water PAHs reported in ng/L) | SYNTHETIC BIOCIDES (Target MDLs: water – 2 pg/L) | OTHER SYNTHETIC COMPOUNDS |
| 1-Methylnaphthalene 2,3,5-Trimethylnaphthalene 2,6-Dimethylnaphthalene 2-Methylnaphthalene Biphenyl Naphthalene 1-Methylphenanthrene Acenaphthene Acenaphthylene Anthracene Fluorene Phenanthrene Benz(a)anthracene Chrysene Fluoranthene Pyrene Benzo(a)pyrene Benzo(b)fluoranthene Benzo(e)pyrene Benzo(k)fluoranthene Dibenz(a,h)anthracene Perylene Benzo(ghi)perylene Indeno(1,2,3-cd)pyrene Dibenzothiophene Alkylated PAHs C1-Chrysenes C2-Chrysenes C3-Chrysenes C4-Chrysenes C1-Dibenzothiophenes C2-Dibenzothiophenes C3-Dibenzothiophenes C1-Fluoranthene/Pyrenes C1-Fluorenes C2-Fluorenes C3-Fluorenes C1-Naphthalenes C2-Naphthalenes C3-Naphthalenes C4-Naphthalenes C1-Phenanthrene/Anthracenes C2-Phenanthrene/Anthracenes C3-Phenanthrene/Anthracenes C4-Phenanthrene/Anthracenes | Cyclopentadienes Aldrin Dieldrin Endrin Chlordanes alpha-Chlordane cis-Nonachlor gamma-Chlordane Heptachlor Heptachlor Epoxide Oxychlordane trans-Nonachlor DDTs o,p’-DDD o,p’-DDE o,p’-DDT p,p’-DDD p,p’-DDE p,p’-DDT HCH alpha-HCH beta-HCH delta-HCH gamma-HCH Other Synthetic Biocides Chlorpyrifos (water only; CDFG-WPCL) Dacthal (water only) Diazinon (water only; CDFG-WPCL) Endosulfan I (water only) Endosulfan II (water only) Endosulfan Sulfate (water only) Hexachlorobenzene Mirex Oxadiazon (water only) | PCB congeners (IUPAC numbers) (Target MDLs: water – 2 pg/L) 8, 18, 28, 31, 33, 44, 49, 52, 56, 60, 66, 70, 74, 87, 95, 97, 99, 101, 105, 110, 118, 128, 132, 138, 141, 149, 151, 153, 156, 158, 170, 174, 177, 180, 183, 187, 194, 195, 201, 203 Polybrominated Diphenyl Ethers (BDE-IUPAC No., Compound Name) (Target MDLs: water – 1 pg/L). BDE 17 [2,2’,4-triBDE] BDE 28 [2,4,4’-triBDE] BDE 47 [2,2’,4,4’-tetraBDE] BDE 66 [2,3’,4,4’-tetraBDE] BDE 82 [2,2’,3,3’,4-pentaBDE] BDE 85 [2,2’,3,4,4’-pentaBDE] BDE 99 [2,2’,4,4’5-pentaBDE] BDE 100 [2,2’,4,4’,6-pentaBDE] BDE 128 [2,2’,3,3’,4,4’-hexaBDE] BDE 138 [2,2’,3,4,4’,5’-hexaBDE] BDE 153 [2,2’,4,4’,5,5’-hexaBDE] BDE 154 [2,2’,4,4’,5,6’-hexaBDE] BDE 183 [2,2’,3,4,4’,5’,6-heptaBDE] BDE 190 [2,3,3’,4,4’,5,6-heptaBDE] Octa-BDE Nona-BDE BDE 209 [2,2’,3,3’,4,4’,5,5’,6,6’-decaBDE] |